## Slide 1: TLV_Logistics
2023

## Slide 2: preprocessing
supply:
  download prika point and line layers from iview
  do not use line layer
  point shp layer files to csv
  process sign text in xlsx to extract prika length in meters and hours in week
  AP manual process of signs that failed auto process
  missing step to fill in meters when till next intersection or next sign
  fill in default values for meters and hours where missing
  factor 24h signs for relevant hours in week
  remerge (join) location of signs based on id
demand for on-street delivery:
  start with business layer with weekly delivery demand
  filter out items that have weekly delivery value of zero
  filter out hotels with more than 3 stars (assume dedicated on-site delivery spaces)
  filter out businesses in big merkazim_mischariim (assume dedicated on-site delivery spaces)
  filter or fix (geo-code from address) missing x / y coordinates

## Slide 3: flow snap100
supply: Trafic Signs Points prika ve teina v5s_ap
demand: tlv_businesses_w_logistics_filtered
snap100 to cf segments:
  Trafic Signs Points prika ve teina snap100 cf
  tlv_businesses_w_logistics snap100 cf
buff5 cf: cf_1_2_buf5
count supply points (weight: hours_x_meters) in cf_1_2_buf5:
  cf_1_2_snap100_supply_v5s_ap
count demand points (weight: תדירות הפצה שבועית) in cf_1_2_snap100_supply_v5s_ap:
  cf_1_2_snap100_supply_demand_v5s_ap
buff20 to total of 25:
  cf_1_2_snap100_supply_demand_v5s_ap_buff25
    compute supply vs demand : (supply_count / 6) / demand_count [spaces_x_ weekly_hours / deliveries per week]
project geojson to 4326 for input to leaflet
convert geojson to js for input to leaflet

## Slide 4: v1
the segments are from the commercial front layer
the supply is based on the manually updated file you sent me
the default for missing prika length is 12meters (can be changed)
the default for missing hours is 36 hours a week (can be changed)
no limit hours (24 hours a day) is counted as 6 * 24 hours per week (can be changed)
the buffer used to sum the supply and the demand is 200meters
the total average supply to demand ratio is 3.0 [meters * weekly hours / weekly deliveries] (which is equivalent to 6meters for 30min per delivery
so in the map a supply to demand ratio less than 3 is below average and higher than 3 is above average...
in order to improve the supply data we need a layer with street directions (till the next intersection... and the rest of the signs to take into account canceling signs...
another potential improvement in the map analysis is to snap the supply and demand points to the nearest street segment before summing... this deals with double counting...
in addition we could take excess parking areas into consideration as supply...
also, I think we need to add underground delivery supply for the big commercial centers...
let me know how best to proceed... or call to discuss...

## Slide 5
IView
Trafic Signs Points prika ve teina.shp
Trafic Signs Lines prika ve teina.shp
QGIS
Trafic Signs Points prika ve teina.csv
Trafic Signs Lines prika ve teina.csv